## Slide 1: Apollo Business Consulting Network Design Proposal
shana.
NETWORKS

## Slide 2: Apollo: Innovation, Collaboration, & Excellence
311 active employees
Provide innovative solutions to everyday business problems
Operates several in-house servers
  Provide various web-based applications and services
Plans to expand into a new future-forward 5 floor facility
  Will need a robust, scalable network to support this growth…
shana.
NETWORKS

## Slide 3: Agenda
Proposed network solution to support Apollo’s relocation.
Three-layer network design
  Core / Distribution / Access level hardware
  Cabling summary
  Overview of proposed logical / physical designs
  Cost Breakdown
An industry leading network that will scale with you!
shana.
NETWORKS

## Slide 4: Hardware
Scott Richards
shana.
NETWORKS

## Slide 5: Core / Distribution
  Cisco Catalyst 9300X – 24 Port (C9300X2-24Y) (3x)
    Built for enterprise grade security and scalability
    Flexible modular uplinks of either 100, 40, 24, 10, or 1 Gbit
    11 integrated routing protocols
    Private VLAN functionality
    Built for expansion
      Stackable and backwards compatible
  Our design implements 3
    One for core, two for distribution
    Will provide nearly twice the required uplink per distribution trunk (~12.6 Gbit/s)
shana.
NETWORKS

## Slide 6: Access LEvel
  Cisco Business 350 Series
    CBS350-48FP-4X x8
    CBS350-24FP-4X x8
    CBS350-8FP-E-2G x5
  Managed, stackable, feature-packed
    POE+ on every port
    Policy based routing
    VLAN support
  4x 10Gbit SFP+ uplinks to serve a max department bandwidth of ~3.3Gbit/s
shana.
NETWORKS

## Slide 7: Firewall and Optional WLC
  Cisco FirePOWER 3140 Next Gen Firewall (FPR3140-NGFW-K9) (1x)
    48 Gbit throughput, industry leading security features.
  Cisco Catalyst 9800 Wireless Controller (C9800-40-K9) (1x)
    Robust and secure, capable of controlling up to 2000 Aps
    See report for details on wireless option
shana.
NETWORKS
Firewall WLC

## Slide 8: Cabling
Neil Power
shana.
NETWORKS

## Slide 9: Floor 1
shana.
NETWORKS

## Slide 10: Floor 2
shana.
NETWORKS

## Slide 11: Cabling
shana.
NETWORKS
Placement | Type | Total Length | Cost Estimate
Work Area | Category 6 | 1691 meters | ~$4,633.34
Horizontal | Category 6 | 11792 meters | ~$124,363.35
Backbone | Multi-mode Fiber | 345 meters | ~$3,057.60
TR Patch Cables | Cat6/Fiber | 163 meters | ~$1,040.45

## Slide 12: Cabling
shana.
NETWORKS

## Slide 13: Layout & Logic
Adam Lo Giudice
shana.
NETWORKS

## Slide 14: Logical Map
shana.
NETWORKS

## Slide 15: Logical Map
shana.
NETWORKS

## Slide 16: Logical Map
shana.
NETWORKS

## Slide 17: Logical Map
shana.
NETWORKS

## Slide 18: Logical Map
shana.
NETWORKS

## Slide 19: Cost-Analysis
Henry Oyewole
shana.
NETWORKS

## Slide 20: Cost-Analysis
  Provided hardware is of the highest grade
    Will allow for scalability and expansion as needed
  Room for adjustment as per Apollo’s requirements / budget flexibility
    May reduce cost but…
    We recommend this configuration for adoption
Total acquisition cost: $531,639.35
Yearly upkeep: $2,712.00
shana.
NETWORKS

## Slide 21: Cost Breakdown
shana.
NETWORKS

## Slide 22: Conclusion
Antonio Giacchetti
shana.
NETWORKS

## Slide 23: Thank You!
Network Infrastructure COMP 10019 Group 12 * not implemented
shana.
NETWORKS
www.shana.com * business@shana.com *